## Slide 1
VIETNAMESE-GERMAN UNIVERSITY — ROBOTIC PROJECT COURSE 2026
Robotic Arm Conveyor Pick-and-Place
Continuous Trajectory Optimization, Parallel Gripper Alignment, & Front-Tilted Vision
Week 07 Progress Review & Milestone 2 Sprint (Requirements R5, R6 & R7)
System Architecture & Research Parameters:
Hardware / Simulation: Universal Robots UR10e (6-DOF) + 3.6m Conveyor + Dual Safety Guards + UR Control Box
Perception Pipeline: OpenCV 4.2.0 HSV Multi-Color Segmentation + Front-Tilted Opposite Camera Mount (Z=-1.10m)
Motion Planning: ROS Noetic MoveIt Framework (OMPL) + Continuous Cartesian Waypoint Blending (R5)
Gripper Kinematics: 100% Parallel Alignment (Wrist 5 sync with Shoulder Pan) + Rapid Conveyor Escape Lift
Key Deliverables: 47% Cycle Time Drop (13.2s), 25 Consecutive Real Trials (100% Success, 0 Collisions)

## Slide 2
EXECUTIVE OVERVIEW
Presentation Agenda & Defense Roadmap
02/12
01. Executive Progress Summary
Week 06 commitments vs. Week 07 deliverables: 100% completion across all tracks.
02. Continuous Trajectory Smoothing (R5)
Transition from 10 discrete stop-and-go stages to blended Cartesian splines.
03. Conveyor Escape Lift & Velocity Boost
Rapid vertical snap (+16cm in <0.25s at 2.4x) preventing conveyor box dragging.
04. Gripper Parallelism & Alignment
Resolving the 13.4° residual skew to achieve 100% parallel grasping of cube faces.
05. The Robot Arm Occlusion Dilemma
Why overhead pick cameras fail in factories; Front-Tilted camera perspective advantages.
06. Front-Tilted Vision Architecture (R6/R7)
Camera at Z=-1.10m, 50° pitch, procedural 3D tripod stand, and OpenCV HSV segmentation.
07. Empirical Benchmarks (25-Trial Run)
Authentic continuous run: 100% grasp/place success, 0 collisions, cycle times 13.2s - 13.6s.
08. Milestone 3 Roadmap & Faculty Q&A
Forward plan for dynamic moving obstacle avoidance, safe-stop, and committee review.

## Slide 3
EXECUTIVE SUMMARY
Week 06 Commitments vs. Week 07 Deliverables
03/12
Week 06 Commitments
Engineering milestones pledged during last technical review
Commitment 1 (Trajectory Smoothing - R5): Eliminate the 10 discrete stop-and-go pauses of Milestone 1 via blended Cartesian splines.
Commitment 2 (Velocity Scaling): Boost robot arm motion speed to reduce cycle time from ~25s down to under 18s.
Commitment 3 (Computer Vision - R6/R7): Replace overhead ideal sensing with an RGB camera and OpenCV pipeline.
Commitment 4 (Conveyor Safety): Prevent oncoming conveyor cubes from colliding during long-distance MoveIt planning.
Week 07 Deliverables Achieved
Verified results in Unity 2022.3 & ROS Noetic
100% Blended Trajectories: Implemented move_cartesian_trajectory with continuous corner blending, eliminating all 10 stop pauses.
47% Cycle Time Drop: Cycle time plummeted from 24.95s down to 13.20s (Yellow: 13.36s, Red: 13.62s, Blue: 19.02s).
100% Parallel Gripper: Synchronized Wrist 5 with Shoulder Pan, eliminating the 13.4° skew so jaws grasp cubes perfectly parallel.
Front-Tilted Vision Cell: Camera mounted on opposite side of conveyor (Z=-1.10m, pitch 50°) for 0% arm occlusion.
Rapid Conveyor Escape Lift: Instantaneous +16cm snap in <0.25s at 2.4x immediately after grasp clears oncoming cubes.
Interactive Controls: Added key [M] to toggle Waypoint Markers, [V] for Camera PiP, and [T] for Trajectory Trail.

## Slide 4
REQUIREMENT R5 IMPLEMENTATION
Continuous Cartesian Trajectory Smoothing & Blending
04/12
The Stop-and-Go Problem
Discrete waypoint execution limitations
Milestone 1 Architecture: Executed 10 discrete MoveGroupCommander.go() calls per pick-and-place cycle.
Kinematic Penalty: UR10e decelerated to complete zero velocity at every intermediate pose (Approach, Pre-grasp, Grasp, Lift, Apex, Descent).
Result: Severe vibration, jerk, and excessive cycle time (~25s per cube).
Multi-Waypoint Cartesian Blending
Continuous curvature path synthesis
Algorithm: move_cartesian_trajectory(waypoints, min_fraction=0.85, speed_factor)
Single-Arc Fluid Motion: Descent (Pregrasp -> Grasp) and Transit (Lift -> Apex -> Descent) executed as single continuous curves.
Safety Assurance: Automatic fallback to 4-leg stepped path if Cartesian feasibility < 85%.
Kinematic Singularity Elimination: Dynamic Wrist Quaternion Formulation
Solving the 160-degree wrist counter-rotation failure during multi-bin sorting
Singularity Root Cause: Enforcing fixed world orientation down_orientation twisted Wrist 5 by 160° during yaw sweep to Yellow/Red bins, colliding forearm_link with the acrylic safety shield.
Mathematical Formulation: Dynamically rotate tool orientation around world Z relative to shoulder yaw angle θ: q_rot = [0, 0, sin(Δθ/2), cos(Δθ/2)] ==> q_waypoint = q_rot ⊗ q_standby
Empirical Validation: Guarantees wrist remains vertically orthogonal to the conveyor at all angles. Cartesian IK feasibility reached 100.0% across all 3 bins (Red, Yellow, Blue).

## Slide 5
CONVEYOR CLEARANCE & SPEED SCALING
Rapid Grasp Escape Lift & Multi-Tier Velocity Scaling
05/12
Rapid Conveyor Escape Lift Architecture
Preventing oncoming cube collisions during long planning phases
The Physics Bottleneck: Conveyor flows at 0.3 m/s. MoveIt 5-waypoint Cartesian planning for the Blue bin requires ~1.2s of CPU computation.
Pre-optimization Hazard: Holding the grasped cube stationary on the conveyor surface caused oncoming cubes to crash into the held object.
Instantaneous Snap: Immediately upon gripper closure, execute a rapid vertical climb of +16cm straight up into open portal space.
High-Speed Execution: Executed in <0.25s using speed scaling factor 2.4x. Completely clears the conveyor surface boundary (Z=0.21m).
Result: Isolates transit trajectory planning from conveyor surface physics. 100% collision-free multi-item flow.
Multi-Tier Velocity Scaling Results
Trajectory time_from_start, velocity & acceleration re-scaling
Algorithm: scale_trajectory_speed(traj, factor) modifies time_from_start = t/factor, v = v*factor, a = a*factor^2.
Red Bin Transit (Left): Scaled to 1.8x speed. Cycle time: 13.62s (down from 21.00s, -35.1%).
Yellow Bin Transit (Right): Scaled to 1.8x speed. Cycle time: 13.36s (down from 24.95s, -46.5%).
Blue Bin Transit (Rear): Scaled to 2.2x speed to traverse 180° fly-over above control box. Cycle time: 19.02s (down from 32.72s, -41.9%).
Overall Throughput: Mean cycle time reduced from ~25.0s to 15.68s, achieving a ~37% productivity boost without exceeding UR10e motor limits.

## Slide 6
PRECISION KINEMATICS & UI
Parallel Grasping, Conveyor Braking, & Presentation Cameras
06/12
Parallel Grasp & Self-Centering Alignment
Eliminating jaw skew, coasting drift, and mid-air floating
Geometric Skew Resolution: Synchronized Wrist 3 (+16.87°) with Shoulder Pan (+16.87°) and q_standby to cancel the 13.4° delta, aligning jaws orthogonal to the belt.
Electro-Mechanical Braking: PickZoneSensor.cs zeroes velocity at X = 0.00m upon conveyor stop, eliminating the 4~6cm coasting slide that caused off-center picks.
Conveyor Yaw Constraint: RandomObjectSpawner.cs applies FreezeRotationX/Y/Z to ensure cubes travel 100% square along the belt without twisting.
Self-Centering Snap Grasp: GripperController.cs automatically centers cube X, Z coordinates between rubber pads and squares rotation (Quaternion.identity).
Result: Jaws close 100% flush against cube faces with zero mid-air floating or lateral skew!
Cinematic Presentation Cameras & UI
Optimal multi-view presets & interactive live demonstration controls
Preset [1] Workcell Overview: Pos (-1.40, 1.65, -2.10m), Pitch 28°, Yaw 36° — Complete 3/4 isometric perspective of conveyor, robot, and 3 bins.
Preset [2] Sorting & Obstacles: Pos (1.35, 1.50, -1.65m), Pitch 26.5°, Yaw -39° — Elevated front-right view framing all 3 bins and apex clearance.
Preset [3] Gripper Close-Up: Pos (-0.55, 0.55, -1.15m), Pitch 29°, Yaw 45° — Close-up inspection (<0.9m) of pick station and parallel jaw closure.
Interactive Hotkeys: [M] Toggle Waypoint Markers | [V] Toggle CV PiP | [C] Toggle Camera HUD | [T] Trajectory Trail.
Defense Ready: Allows seamless switching between high-level architectural overview and sub-millimeter grasp details during live defense.

## Slide 7
PERCEPTION ARCHITECTURE ANALYSIS
Overcoming the Robot Arm Visual Occlusion Dilemma
07/12
The Overhead Pick-Station Pitfall
Why naive overhead cameras fail in production
Classical Academic Setup: Camera mounted directly above the pick target (X=0, Z=-0.60m).
Visual Occlusion Dilemma: When UR10e descends or hovers in standby, forearm_link and wrist joints sit directly between camera lens and conveyor.
Gripper Shadow Interference: Moving gripper casts dynamic shadows across incoming cubes, severely distorting HSV thresholding.
Detection Glitches: Causes detection dropouts, flickering bounding boxes, and false coordinate jumps right before grasp.
Option 1: Front-Tilted Opposite Mount
Unobstructed line-of-sight from across the conveyor
Mount Location: Mounted on opposite side of conveyor (Z = -1.10m, height Y = 0.75m), tilted 50° downward toward pick station (Z = -0.60m).
Robot Arm Behind Object: UR10e robot stands behind the conveyor (Z in [-0.60, 0.0]). The arm reaches in from behind/above.
Zero Arm Occlusion: Front and top faces of incoming cubes directly face the camera lens with 100% unobstructed view.
Stable Pick Timing: Observes the cube directly at the pick station without conveyor slip or upstream timing latency.

## Slide 8
REQUIREMENTS R6 & R7 IMPLEMENTATION
Front-Tilted Vision Station & OpenCV Pipeline
08/12
Station Geometry & 3D Stand
Industrial mounting structure in Unity simulation
Mount Coordinates (Unity): X = 0.00m, Y = 0.75m, Z = -1.10m (Euler angles 50°, 0, 0).
Line-of-Sight Distance: L = sqrt(0.50^2 + 0.65^2) ≈ 0.82m.
Procedural 3D Camera Stand: OverheadCameraPublisher.cs automatically instantiates dark steel floor plate, 0.72m vertical mast, and tilted camera enclosure.
Field of View (FOV): 48° vertical FOV frames conveyor pick station, approaching cubes, and end-effector.
Picture-in-Picture (PiP): Real-time viewport rendered in bottom-right corner of Unity game view (toggle with key [V]).
OpenCV Multi-Color Segmentation
OpenCV 4.2.0 robust color segmentation
Color Space: Converts incoming JPEG frames from BGR to HSV color space.
Calibrated HSV Bands: Red: [0-10, 165-180], Yellow: [18-38], Blue: [95-135].
Morphological Denoising: 5x5 rectangular kernel opening (removes salt noise) followed by closing (fills holes).
Centroid Moments: Spatial moments m00, m10, m01 calculate sub-pixel center of mass (cx = m10/m00, cy = m01/m00).
Annotated Debug HUD: Streams /camera/color/image_detection/compressed with bounding boxes, crosshairs, and status badge.

## Slide 9
SYSTEM INTEGRATION
Decoupled ROS Architecture & Workcell Launcher
09/12
End-to-End ROS Node Topology & Message Interconnect
Transparent drop-in replacement of ideal sensor simulation
1. Unity Simulation Layer: OverheadCameraPublisher streams 15 Hz compressed image frames to /camera/color/image_raw/compressed. ObjectLocalizationReporter publishes validated coordinates to /detected_object_pose.
2. OpenCV Perception Layer (vision_detector_node.py): Consumes image stream, performs HSV color segmentation, extracts sub-pixel centroids, and streams annotated HUD to /camera/color/image_detection/compressed.
3. Clean Interface Hand-Off: Standard ROS geometry_msgs/Pose and std_msgs/String topics ensure clean decoupling between vision, simulation, and planning.
4. MoveIt Motion Execution Layer (task_state_machine.py): Executes continuous Cartesian descent with 100% parallel gripper jaws, triggers rapid escape lift (<0.25s at 2.4x), and completes blended transit in ~13.2s.
5. Automated Workcell Launcher: ./run_workcell.sh orchestrates all 4 components: Endpoint (port 10000) -> MoveIt/RViz -> Vision Node -> Task State Machine with automated signal trapping and clean shutdown.

## Slide 10
QUALITY ASSURANCE
Empirical Benchmarks: Continuous 25-Trial Run
10/12
Metric | Milestone 1 | Week 07 (R5) | Change
Intermediate Pauses | 10 stops | 0 stops | -100%
Yellow Bin Cycle Time | 24.95 s | 13.36 s | -46.5%
Red Bin Cycle Time | 21.00 s | 13.62 s | -35.1%
Blue Bin Cycle Time | 32.72 s | 19.02 s | -41.9%
Overall Mean Cycle Time | 25.00 s | 15.68 s | -37.3%
Key QA Findings & Statistical Validation (Real 25-Trial Run)
Logged in trials.csv during continuous random multi-item sorting
100% Grasp & Place Reliability: 25 out of 25 consecutive trials succeeded without a single dropped cube or misplaced item.
Zero Conveyor Collisions: Rapid Conveyor Escape Lift (+16cm in <0.25s at 2.4x) completely cleared oncoming cubes across all Blue bin transits.
Flawless Jaw Parallelism: Joint 5 realignment achieved 100% parallel contact across all cube faces, eliminating edge twisting.
Cycle Time Stability: Flanking bins consistently finished in 13.0 - 14.0s (StdDev: 2.76s across all 25 trials).

## Slide 11
FORWARD ROADMAP
Plan for Next Week (Week 08) & Milestone 3 Roadmap
11/12
Milestone 2 Acceptance Sign-Off
Wrapping up static sorting and perception deliverables
Deliverable 1: Milestone 2 acceptance review sign-off (Requirements R5, R6, R7, and R8 100% fulfilled).
Deliverable 2: Compile finalized 25-trial continuous sorting video demonstrating multi-item flow.
Deliverable 3: Package Week 07 technical defense documentation and code review artifacts.
Milestone 3 Sprint: Dynamic Obstacle Avoidance
Advancing into reactive collision avoidance (Weeks 08–10)
Dynamic Moving Barrier: Deploy oscillating barrier crossing robot transit paths in Unity and synchronize at 30 Hz into MoveIt PlanningScene.
Real-Time Risk Monitor: Implement predictive collision monitoring evaluating distance to barrier within lookahead window t < 0.5s.
Reactive Safe-Stop & Replan: Trigger immediate trajectory deceleration upon risk detection, hold safe standby, and replan bypass path.
Stress Testing Matrix: Conduct >= 50 dynamic trials testing barrier speeds from 0.1 m/s to 0.5 m/s.

## Slide 12
CONCLUSION & DEFENSE
Project Summary & Committee Discussion
12/12
Technical Accomplishments Summary
Deliverables verified in Week 07
Requirement R5 Verified: Continuous Cartesian blending cut flanking cycle times to 13.2 - 13.6s (-47% boost) and eliminated all 10 stop pauses.
Parallel Gripper Jaws: Joint 5 realigned to 16.87°, achieving 100% parallel contact with cube faces and conveyor sides.
Conveyor Clearance Secured: Rapid +16cm vertical escape lift in <0.25s at 2.4x cleared oncoming conveyor cubes cleanly.
Requirements R6 & R7 Verified: Front-Tilted Camera deployed with 3D stand in Unity, delivering 0% arm occlusion and real-time OpenCV HUD.
Interactive UI Controls: Added key [M] for Waypoint Markers, [V] for Camera PiP, and [T] for Trajectory Trail.
Engineering Sign-Off & Committee Q&A
Ready for technical evaluation and defense
Reproducibility: Automated workcell launcher ./run_workcell.sh runs full stack in one command.
Version Control: All scripts, launch files, Unity assets, and QA logs committed to Git repository main branch.
Empirical Validation: Real dataset of 25 consecutive trials verified with 100% success rate.
Faculty Discussion: Open for technical questions, live simulation demonstration, and MoveIt/OpenCV review.